## Slide 1
Haptic Particle Simulations
M.Tech 1st Stage Project
Dwaipayan Sardar * | 143079009
GUIDE: Prof. Subhasis Chaudhuri *
EXAMINAR: Prof. Abhishek Gupta #
* - Department of ElectricalEngineering, IIT Bombay
# - Department of Mechanical Engineering, IIT Bombay
R. Winchenbach and et al, “Constrained Neighbor Lists for SPH-based Fluid Simulations“, ACM SIGGRAPH 2016
VIP Lab
EE, IIT Bombay

## Slide 2
Motivation
It’s need:
  Natural alike interactive simulation
  Particle dynamics is favorable in modelling a wide variety of objects [Macklin ‘14]
  Adds an edge in fluid and deformable object rendering
  Above materials finds use in tissue & bio-fluid modelling and VR games
How it is achieved?
  DEM and SPH techniques for particle physics modelling
  Considering independent particles: leveraging extensively parallel GPU architecture
  High DoF Haptics point devices and open source C++ libraries fro interfacing them

## Slide 3
Particle simulations: overview
Obejective: Simulation of fluids composed of particles
Methods:
  Discrete Element Modelling – Lagrangian based
Assumptions:
  A set of particles enclosed in a hollow volume
  Collide inelastically with immediate neighbors: particles, colliders and bounding walls
  No gravitational attraction is considered among the particles, though a constant global gravity affects the overall system
  A global damping is added to render a smooth effect of atmosphere
Eulerian | Lagrangian
Workspace is discretised into grid | Material is discretised into particles
Compute properties at all grid points | Perform computation wherever necessary

## Slide 4
Particle simulations: physical modelling
Independence of calculations DEM
PA
PB
VA
VB
PAB
B, RB
A, RA
FP
|PAB|
VABTan
VAB
VABNor
Fa
Fsh
O

## Slide 5
Simulation forces:
Forming small deformable clusters of particles
Constructing isosurfaces of clusters:
Challenges in real time:
Fluid seen as particles
https://developer.nvidia.com/content/fluid-simulation-alice-madness-returns
Pressure | Viscosity | Surface tension | Interactions
Marching Cubes | Point Splats
Large no. of particles | Numerous terms in Navier Stokes Eq.
Interactive speed | Handled by independent threads

## Slide 6
Introduced in ’70s to simulate astronomical fissions and collisions [Lucy, Gingold]
People utilized it to simulate flow: fluidic, granular or even deformable objects
Quantities derived from neighbors by interpolating
Density formulation:
Smoothed quantity:
Kernels are smoothening functions:
Various forces are smoothed according to the complexity of fluid, or granularity, and added to NSE
SPH: introduction

## Slide 7
Navier-stokes equations (NSE) for in-compressible flow:
SPH approximates NSE on a set of particles: providing fluid appearance [Muller 03]
For an instant of time the spatial derivative only affects kernel (spatially varying)
SPH: Navier-Stokes equations

## Slide 8
Pressure:
Viscous force:
Surface tension:
  Where:
Adhesion:
SPH: forces in N-S equations

## Slide 9
User interactions
  Challenges in real time:
    Visual interface ~ 30 – 60 fps {mouse keyboard}
    Haptic interface ~ 500 – 1000 KHz {Novint Falcon(3DoF)}
  f term in NSE takes care of this force
  Haptics incorporation:
    Hardware update rate kept constant at 1000KHz
    Still force update rate is limited by rendering lag
    Can be reduced by
M.Tech 1st Stage Electrical Engineering, IIT Bombay

## Slide 10
Fluid – rigid interaction
  Forces and torques
  Haptics incorporation
M.Tech 1st Stage Electrical Engineering, IIT Bombay

## Slide 11
Implementation – steps
Collision Processing { accumulate force from neighbors, collider, walls }
Pressure (damped spring)
Shear (viscosity)
Integration { position ← velocity ← force }
Change in velocity ← accumulated force
Position ← simulation time step * velocity
Grid update { position and velocity are sorted according to grid index }
Fast radix sorting and update to new
Improve memory access coherence
Attraction (after collision)
If proxy collision detected: non-zero collider forces sent to host for accumulation

## Slide 12
Implementation – source of forces I
  Pressure, collide attraction {adhesion} and shear {viscosity} from other particles
  DEM :
  Forces interpolated from box kernel :
  Max 26 immediate neighbors of each :
  Influence: Iff nbd ≠ empty :
  Nbd forces accumulated :
  SPH with forces* from nbd with box kernel ↔ DEM
* Forces integrated to attributes, interpolated to fixed grid position. Forces composed of pressure, viscosity and adhesion
Pi

## Slide 13
Implementation – source of forces II
  Pressure, collide attraction {adhesion} and shear {viscosity} from collider
Pi
Wall
FP
Pressure from boundary walls | Collider force
Damped spring force | Pressure, attraction and shearing
Pi
Ci

## Slide 14
Implementation – CUDA
  Particle attributes {graphical rendering} : sorted position and velocity
  Collider attribute {haptic rendering} : force from particle collision
  Independent CUDA threads computed at one time instant
  Particles : accumulated forces integrate to attributes
  Collider : accumulated forces sent to haptic rendering
  Particle attribute calculation : occupy one CUDA thread per particle
  Collider force accumulation : occupy one CPU thread
  Grid interpolation & sorting : occupy one CUDA thread per particle

## Slide 15
Implementation – steps
Collision Processing { accumulate force from neighbors, collider, walls }
Pressure (damped spring)
Shear (viscosity, friction)
Integration { position ← velocity ← force }
Change in velocity ← accumulated force
Position ← simulation time step * velocity
Grid update { position and velocity are sorted according to grid index }
Fast radix sorting and update to new
Improve memory access coherence
Attraction (after collision)
If proxy collision detected: non-zero collider forces sent to host for accumulation

## Slide 16
Implementation: graphical rendering
Particle attribute calculation
Grid interpolation and sorting without transferring to host
Storing attributes in device memory, to send directly for graphical rendering
Positions allocated as float4arrays, in OpenGL vertex array object (VBO)
VBO is mapped for use by CUDA GL for rendering @ 20-100 fps

## Slide 17
Implementation: haptic rendering
A haptic force field is constructed from collider force
Force field is buffered and fed to a Novint Falcon haptic device
Collider attribute calculation in a cpu thread

## Slide 18
Implementation: Results – I
10,000 particles ~ 48fps
A ball of particles dropped on collider (proxy)
Particle clusters on bouncing
Some particle cling to collider (sticky)
User gets haptic feedback

## Slide 19
Implementation: Results – II
User haptic interaction

## Slide 20
Results: Comparison
SPH in haptic rendering of dental filling materials [Brian ‘15]:
  2,000 particles ~ 447fps
  Dual GTX GPU: SPH calculation, graphical rendering
Six DoF haptic rendering with fluids and solids [Cirio ’11]
  Restricted nbd* to 26 immediate particles {same as our box nbd*}
  32,000 fluid particles ~ 70fps; rigid bodies doesn’t take much time to render
  Quadro GPU: SPH calculation
Our work [ongoing]:
  10,000 particles ~ 50fps, 32-bit API, other optimizations yet to apply
  Both DEM calculation in box nbd* and graphical rendering in single GPU
*nbd = neighborhood

## Slide 21
Future aspects: SPH and graphics
  Work upgrade : fluid surface reconstruction : construct iso-surfaces
            : 32-bit simulation {HAPI} : slow, recent CUDA not supported
            : 64-bit support : OpenHaptics toolkit
  DEM–SPH coupling : force interpolation from nbd using discussed kernels after DEM
  Granular material : surface friction [Otaduy ‘11] : pressure but no attraction (adhesion)
            : velocity damping : dissipates kinetic energy
  Fluids : surface tension {SPH}
            : adhesion {SPH} instead of collide attraction

## Slide 22
Proposals: interactive haptic mixing
M.Tech 1st Stage Electrical Engineering, IIT Bombay
  Unified particle modelling for various objects {different liquids, solids, granular material}
  Interactive fluids mixing
  Granular solids mixing with fluids
  Pouring of fluid on a concave bowl held {haptic} by user
  Deformable object interaction constraints:
    bounded particle position
    high adhesion
    high velocity damping, and more to find out
Fluids | Solids | Granular flow
Different fluids: density (mass), pressure, adhesion (Ka), tension (γ), viscosity (µ) | Fixed relative position of particles, constant density Forces and torque act on CoM | pressure friction wall friction

## Slide 23
Thank you

## Slide 24
All kernels are discussed by Muller[2] and Brian [8]
Density and surface tension kernel
Pressure kernel
Viscosity kernel
Adhesion kernel
SPH: kernels

## Slide 25
Building uniform grids

## Slide 26
Simulation parameters
  Grid size vs particle size choice and collider choice

## Slide 27
PA
PB
VA
VB
PAB
B, RB
A, RA
FP
|PAB|
VABTan
VAB
VABNor
Fa
Fsh
O

## Slide 28
Pi
Pi
Ci
Pi
Wall
FP

## Slide 29
http://physics.stackexchange.com/users/9887/alfred-centauri
VIP Lab
EE, IIT Bombay

## Slide 30
R. Winchenbach and et al, “Constrained Neighbor Lists for SPH-based Fluid Simulations“, ACM SIGGRAPH 2016

## Slide 32
Collision Processing { accumulate force from neighbors, collider, walls }
Pressure (damped spring)
Shear (viscosity)
Integration { position ← velocity ← force }
Change in velocity ← accumulated force
Position ← simulation time step * velocity
Grid update { position and velocity are sorted according tor grid index }
Fast radix sorting
Improve memory access coherence
Attraction (after collision)
If proxy collision detected: non-zero collider forces sent to host for accumulation